## Slide 1: CIS 565 CUDA Performance Lab
Shehzan Mohammed
@shehzanm

## Slide 2: Today’s List
Lab Algorithms
  Transpose (Contd.)
  Reduction
Nsight Profiler
NVIDIA Visual Profiler(NVVP)
Revisit:
  Memory Coalescing
  Shared Memory
  Bank Conflicts
  Loop Unrolling
Notes: Incorrect launch configuration
ThreadIdx / BlockIdx
Syncthreads
Atomic

## Slide 3: Performance Lab Starter Code
If you completed the transpose kernels – Awesome!
If you did not, no problem – but ask questions if you have.
How many checked the solution branch in Debugging Lab?
Either way, pull the latest master.
  It is updated with the Transpose kernels solutions.

## Slide 4: Memory Coalescing

## Slide 5: Memory Coalescing
Coalesce access to global memory
  Most important performance consideration
  Loads and stores by threads of a warp can be combined into as low as one instruction
The concurrent accesses of the threads of a warp will coalesce into a number of transactions equal to the number of cache lines necessary to service all of the threads
Notes: Threads in a warp are continuous. They execute the same command at the same time.
So why not have them access the same are of the memory. This is memory coalescing and works really fast
Basically says continuous/concurrent memory access is better

## Slide 6: Coalescence
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float each (continuous in memory)
Address fall within 1 L1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%
...
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in sequential order
[i] = [j]
[i+1] = [j+1]

## Slide 7: Coalescence
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float but not sequentially indexed
Address fall within 1 L1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%
...
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in non-sequential order
[i+y] = [j+x]
However, this does not affect performance negatively since we are not using excess memory space.

## Slide 8: Coalescence
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float each (not all continuous in memory)
Address fall within 2 L1 cache-line
  Warp needs 128 bytes
  256 bytes move across the bus on a miss
  Bus utilization: 50%
...
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in sequential order of say alternating elements
This means 256 bytes are fetched although only 128 bytes are accessed.
Why are 256 bytes fecthed? because we are using caches. So continuous data is copied from global to cache and then to threads
[i] = [j]
[i+1] = [j+2]
[i+2] = [j+4]

## Slide 9: Coalescence (Non-cached)
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float each (not all continuous in memory)
Address fall within 5 L2 cache-line
  Warp needs 128 bytes
  160 bytes move across the bus on a miss
  Bus utilization: 80%
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
L1
L2
...
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in sequential order of say alternating elements
This means 160 bytes are fetched although only 128 bytes are accessed.
Why are 160 bytes fecthed? because we are not using caches. So continuous data is copied from global to cache and then to threads
If we were using cache, then 2 L1 blocks would have been occupied which would need 256 bytes to move across the bus.

## Slide 10: Coalescence
A warp requests 1 4-byte word
  All 32 threads requesting 1 float value
Address falls within 1 L1 cache-line
  Warp needs 4 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 3.125%
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: Even though 1 element is access by all threads, the entire memory block needs to be copied
128 bytes in case of L1 and 32 in case of L2

## Slide 11: Coalescence (Non-cached)
A warp requests 1 4-byte words
  All 32 threads requesting 1 float value
Address fall within 1 L2 cache-line
  Warp needs 4 bytes
  32 bytes move across the bus on a miss
  Bus utilization: 12.5%
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
L1
L2
Notes: Even though 1 element is access by all threads, the entire memory block needs to be copied
128 bytes in case of L1 and 32 in case of L2

## Slide 12: Coalescence
A warp requests 32 scattered 4-byte words (random)
Address fall within N L1 cache-line
  Warp needs 128 bytes
  N * 128 bytes move across the bus on a miss
  Bus utilization: 128 / (N * 128)
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
...
Notes: Generalization of cases discussed

## Slide 13: Coalescence (Non-cached)
A warp requests 32 scattered 4-byte words (random)
Address fall within N L1 cache-line
  Warp needs 128 bytes
  N * 32 bytes move across the bus on a miss
  Bus utilization: 128 / (N*32)
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
L1
L2
...

## Slide 14: Shared Memory

## Slide 15: Shared Memory
Acts as a user-controlled cache
Declared using the __shared__ qualifier
Accessible from all threads in the block
Lifetime of the block
Allocate statically or at kernel launch.
__shared__ float myVariable[32];
// ... or specify at launch:
extern __shared__ float myVar[];
myKernel<<<blocks, threads, shared_bytes>>>(parameters);

## Slide 16: Shared Memory
Inter-thread communication within a block
Cache data to reduce redundant global memory access
Improve global memory access patterns
Divided into 32 32-bit banks
  Can be accessed simultaneously
  Requests to the same bank are serialized
Notes: Total shared memory per block depends on GPU, but most have 48K

## Slide 17: Shared Memory
Will revisit….
Notes: Total shared memory per block depends on GPU, but most have 48K

## Slide 18: Matrix Transpose
Notes: Take a paper and write down how much of a speed up you can get over CPU

## Slide 19: Matrix Transpose
Inherently parallel
  Each element independent of another
Simple to implement
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
4 | 8 | 12 | 16

## Slide 20: Matrix Transpose [CPU Transpose]
for(int i = 0; i < rows; i++)
for(int j = 0; j < cols; j++)
transpose[i][j] = matrix[j][i]
Easy
O(n2)
Slow!!!!!!

## Slide 21: Matrix Transpose [Naive GPU Transpose]
GPU Transpose
  Launch 1 thread per element
  Compute index
  Compute transposed index
  Copy data to transpose matrix
O(1) using Parallel compute
Essentially one memcpy from global-to-global
  It should be fast, shouldn’t it?

## Slide 22: Matrix Transpose Let’s make a prediction
Not too different from Memcpy
So if Memcpy is 100% Practical GPU Bandwidth
  How much should we get for transpose?
How much faster than CPU?
Write your answers as percentage

## Slide 23: Matrix Transpose [Naive GPU Transpose]
__global__
void matrixTranspose(float *_a, float *_b) {
int i = blockIdx.x * blockDim.x + threadIdx.x; // row
int j = blockIdx.y * blockDim.y + threadIdx.y; // col
int index_in = j * sizeX + i; // (i, j) from matrix A
int index_out = I * sizeY + j; // transposed index
b[index_out] = a[index_in];
}
2 | 5 | -2 | 6 | 6
3 | 5 | 3 | 4 | 6
4 | 8 | 4 | -1 | 3
2 | 3 | 4
5 | 5 | 8
-2 | 3 | 4
6 | 4 | -1
6 | 6 | 3
_a[ . . . . . .]
_b[ . . . . . .]

## Slide 24: Matrix Transpose [Naive GPU Transpose]
Problems?

## Slide 25: Matrix Transpose [Naive GPU Transpose]
6
5
4
3
2
1
Memory Coalescing – What access patterns are used?
...
...
L1
L2
...
L1
L2
...
...
...
L1
L2
...
L1
L2
...
L1
L2
...
...
L1
L2

## Slide 26: Matrix Transpose [Naive GPU Transpose]
4
2
1
Memory Coalescing – What access patterns are used?
Used for input
Used when writing diag. blocks
Used when writing other blocks
...
...
L1
L2
...
L1
L2
...
L1
L2
...

## Slide 27: G-Mem Access Pattern in Transpose
2 | 3 | 4 | 5 | 5 | 8 | -2 | 3 | 4 | 6 | 4 | -1 | 6 | 6 | 3
2 | 5 | -2 | 6 | 6 | 3 | 5 | 3 | 4 | 6 | 4 | 8 | 4 | -1 | 3
_a
_b
READ - Coalesced memory access
WRITE - Uncoalesced memory access
Good!
Bad!
Notes: Kept this diagram from using earlier
Each element also represents a thread

## Slide 28: Matrix Transpose [Naive GPU Transpose]
Problems?
  Non-coalesced memory
Improvements?
  Want coalesced memory access

## Slide 29: Matrix Transpose [GPU Transpose]
Use Shared Memory
  Allows temporary storage of data
  Use coalesced memory access to global memory
Walkthrough
  Compute input index (same as in naive transpose)
  Copy data to shared memory
  Compute output index
    Remember, coalesced memory access
    Hint, transpose only in shared memory
  Copy data from shared memory to output
Notes: Lets flip it in shared memory
Use __syncthreads

## Slide 30: Memory Access Pattern for Shared Memory Transpose
__syncthreads();
// transpose in shared memory
2 | 3 | 4 | 5
8 | 3 | 5 | 3
1 | 0 | 5 | 9
1 | 9 | 8 | 4
…
…
…
2 | 3 | 4 | 5
8 | 3 | 5 | 3
1 | 0 | 5 | 9
1 | 9 | 8 | 4
2 | 8 | 1 | 1
3 | 3 | 0 | 9
4 | 5 | 5 | 8
5 | 3 | 9 | 4
…
…
…
2 | 8 | 1 | 1
3 | 3 | 0 | 9
4 | 5 | 5 | 8
5 | 3 | 9 | 4
SHARED
MEMORY

## Slide 31: Shared Memory Transpose
Notes: Block is transposed using blockId – Does not affect Global memory access pattern Shared memory transposes within block

## Slide 32: Shared Memory Transpose
__global__ void matrixTransposeShared(const float *_a, float *_b){ __shared__ float mat[BLOCK_SIZE_Y][BLOCK_SIZE_X];
int bx = blockIdx.x * BLOCK_SIZE_X;
int by = blockIdx.y * BLOCK_SIZE_Y;
int i = bx + threadIdx.x; //input
int j = by + threadIdx.y; //input
int ti = by + threadIdx.x; //output
int tj = bx + threadIdx.y; //output
if(i < sizeX && j < sizeY)
mat[threadIdx.y][threadIdx.x] = a[j * sizeX + i];
__syncthreads(); //Wait for all data to be copied
if(tj < sizeY && ti < sizeX)
b[tj * sizeY + ti] = mat[threadIdx.x][threadIdx.y];
}

## Slide 33: Shared Memory Transpose
Problem?

## Slide 34: Shared Memory Transpose
Problem?
  Why are we not even close to max bandwidth?
  Hint, think “banks”
Solution?

## Slide 35: Shared Memory Transpose
Problem?
  Why are we not even close to max bandwidth?
  Hint, think “banks”
Solution?
  Remove bank conflicts

## Slide 36: Bank Conflicts

## Slide 37: Banks
Shared Memory is organized into 32 banks
Consecutive shared memory locations fall on different banks
Warp
__shared__ float tile[64];
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 

## Slide 38: Banks
Access to different banks by
a warp executes in parallel.
__shared__ float tile[64];
int tidx = threadidx.x;
float foo = tile[tidx] - 3;
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 

## Slide 39: Banks
Access to the same element
in a bank is also executed
in parallel.
__shared__ float tile[64];
int tidx = threadidx.x;
int bar = tile[tidx - tidx % 2];
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 
tidx | tidx % 2 | tidx - tidx % 2 | Bank
0 | 0 | 0 | 0
1 | 1 | 0 | 0
10 | 0 | 10 | 10
16 | 0 | 16 | 16
30 | 0 | 30 | 30
31 | 1 | 30 | 30

## Slide 40: Banks
Access to the different elements in a bank is executed serially.
“2 way bank conflict”
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 
__shared__ float tile[64];
int tidx = threadidx.x;
int bar = tile[tidx + tidx % 2 * 31];
tidx | tidx % 2 | tidx % 2 * 31 | tidx + tidx % 2 * 31 | Bank
0 | 0 | 0 | 0 | 0
1 | 1 | 31 | 32 | 0
10 | 0 | 0 | 10 | 10
16 | 0 | 0 | 16 | 16
30 | 0 | 0 | 30 | 30
31 | 1 | 31 | 62 | 30
Notes: Threads want alternate elements which means 2 threads want elements from the same bank

## Slide 41: Banks
Access to the different elements in a bank is also executed serially.
“32 way bank conflict”
b[index_out] = smem[threadIdx.x][threadIdx.y];
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 
tidx | tx [0, 31] | ty [0, 31] | Bank
0 | 0 | Y | Y
1 | 1 | Y | Y
10 | 10 | Y | Y
16 | 16 | Y | Y
30 | 30 | Y | Y
31 | 31 | Y | Y
Notes: All threads want memory from the same bank

## Slide 42: Transpose: Shared Memory
__global__ void matrixTransposeShared(const float *_a, float *_b){ __shared__ float mat[BLOCK_SIZE_Y][BLOCK_SIZE_X];
int bx = blockIdx.x * BLOCK_SIZE_X;
int by = blockIdx.y * BLOCK_SIZE_Y;
int i = bx + threadIdx.x; //input
int j = by + threadIdx.y; //input
int ti = by + threadIdx.x; //output
int tj = bx + threadIdx.y; //output
if(i < sizeX && j < sizeY)
mat[threadIdx.y][threadIdx.x] = a[j * sizeX + i];
__syncthreads
if(tj < sizeY && ti < sizeX)
b[tj * sizeY + ti] = mat[threadIdx.x][threadIdx.y];
}
Represents “row”
Same for all threads in the warp
Represents col and bank number
Represents bank number or “col”
Same for all threads in the warp
Represents entry in the “bank”
Notes: If we look at this code, we notice that threadIdx.x is used as the second index.
We can safely assume that for all threads in the warp, threadIdx.y will be same (because of block size)
Hence, threadIdx.y, which represents the same bank in shared memory, is same for all threads in the warp.
Hence a 32-way bank conflict.

## Slide 43: Transpose: Shared Memory

## Slide 44: Transpose
Reading from input
No Bank conflicts
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 

## Slide 45: Transpose
Writing to output
32-way Bank conflict!!
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 

## Slide 46: Banks
Resolving bank conflict
Elements per row = 32
Shared Mem per row = 33
1 empty element per row
  This is what avoids bank conflicts
// Before
__shared__ float smem[BLOCK_SIZE_Y][BLOCK_SIZE_X];
b[index_out] = smem[threadIdx.x][threadIdx.y];
threadIdx.x | threadIdx.y | Index (Before) | Bank (Before)
0 | Y | 0 * sizeX + Y | Y
1 | Y | 1 * sizeX + Y | Y
10 | Y | 10 * sizeX + Y | Y
16 | Y | 16 * sizeX + Y | Y
30 | Y | 30 * sizeX + Y | Y
31 | Y | 31 * sizeX + Y | Y
Before:
When BLOCK_SIZE_X = 32, sizeX = 32
X * sizeX is always a multiple of 32
Thus, ((X * sizeX) + Y) % 32 banks
Will always result in bank = Y

## Slide 47: Banks
Resolving bank conflict
Elements per row = 32
Shared Mem per row = 33
1 empty element per row
  This is what avoids bank conflicts
// Before
__shared__ float smem[BLOCK_SIZE_Y][BLOCK_SIZE_X];
b[index_out] = smem[threadIdx.x][threadIdx.y];
threadIdx.x | threadIdx.y | Index (Before) | Bank (Before) | Index (After) | Bank (After)
0 | Y | 0 * sizeX + Y | Y | 0 * (sizeX + 1) + Y | Y
1 | Y | 1 * sizeX + Y | Y | 1 * (sizeX + 1) + Y | Y + 1
10 | Y | 10 * sizeX + Y | Y | 10 * (sizeX + 1) + Y | Y + 10
16 | Y | 16 * sizeX + Y | Y | 16 * (sizeX + 1) + Y | Y + 16
30 | Y | 30 * sizeX + Y | Y | 30 * (sizeX + 1) + Y | Y + 30
31 | Y | 31 * sizeX + Y | Y | 31 * (sizeX + 1) + Y | Y + 31
After:
When BLOCK_SIZE_X + 1= 33, sizeX = 32
X * sizeX is never* multiple of 33
Thus, ((X * (sizeX + 1)) + Y) % 32 banks
Will always result in bank = Y + X
// After
__shared__ float smem[BLOCK_SIZE_Y][BLOCK_SIZE_X + 1];
b[index_out] = smem[threadIdx.x][threadIdx.y];
Notes: Never* : except when X = 32, which is fine. Doesn’t cause bank conflict

## Slide 48: Banks
Resolving bank conflict
Elements per row = 32
Shared Mem per row = 33
1 empty element per row
  This is what avoids bank conflicts
Bank 1
Bank 2
Bank 3
Bank 31
Bank 30
Bank 4
Bank 5
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 
__shared__ float smem[BLOCK_SIZE_Y][BLOCK_SIZE_X + 1];
b[index_out] = smem[threadIdx.x][threadIdx.y];

## Slide 49: Transpose: Shared Memory No Bank Conflicts
__global__
void matrixTransposeShared(const float *_a, float *_b){
__shared__ float mat[BLOCK_SIZE_Y][BLOCK_SIZE_X];
__shared__ float mat[BLOCK_SIZE_Y][BLOCK_SIZE_X + 1];
// Rest is the same as regular shared memory transpose
}

## Slide 50: Matrix Transpose [GPU Transpose]
Very very close to production ready!
More ways to improve?
  More work per thread - Do more than one element
  Loop unrolling

## Slide 51: Transpose: Loop Unrolled
More work per thread:
  Threads should be kept light
  But they should also be saturated
  Give them more operations
Loop unrolling
  Allocate operation in a way that loops can be unrolled by the compiler for faster execution
  Warp scheduling
    Kernels can execute 2 instructions simultaneously as long as they are independent

## Slide 52: Transpose: Loop Unrolled
Use same number of blocks, shared memory
Reduce threads per block by factor (side)
Block Size X = 4
Block Size Y = 4
Threads/Block = 16
Total blocks = 2
Shared mem = 4 x 4
Block Size X = 4 -> TILE
Block Size Y = 1 -> SIDE
Threads/Block = 4
Total blocks = 2
Shared mem = TILE x TILE
Notes: Using same number of blocks but using less threads per block.
This means less warps to execute
Note: not all GPUs may see a performance benefit

## Slide 53: Transpose: Loop Unrolled
Walkthrough
Host:
  Same number of blocks
  Compute new threads per block
Device:
  Allocate same shared memory
  Compute input indices similar to before
  Copy data to shared memory using loop (k)
    Unrolled index: add k to y
  Compute output indices similar to before
  Copy data from shared memory into global memory
    Unrolled index: add k to y

## Slide 54
template<int TILE, int SIDE> //TILE = 32, SIDE = 8
__global__ void matrixTransposeUnrolled(const float* a, float* b) {
//Allocate appropriate shared memory (avoid bank conflict)
__shared__ float mat[TILE][TILE + 1];
//Compute input index
int x = blockIdx.x * TILE + threadIdx.x;
int y = blockIdx.y * TILE + threadIdx.y;
//Copy data from input to shared memory. Multiple copies per thread.
#pragma unroll
for (int k = 0; k < TILE; k += SIDE) {
if (x < sizeX && y + k < sizeY)
mat[threadIdx.y + k][threadIdx.x] = a[((y + k) * sizeX) + x];
}
__syncthreads();
//Compute output index
x = blockIdx.y * TILE + threadIdx.x;
y = blockIdx.x * TILE + threadIdx.y;
//Copy data from shared memory to global memory. Multiple copies per thread.
#pragma unroll
for (int k = 0; k < TILE; k += SIDE) {
if (x < sizeY && y + k < sizeX)
b[(y + k) * sizeY + x] = mat[threadIdx.x][threadIdx.y + k];
}
}
Transpose: Loop Unrolled
Code

## Slide 55: Performance for 4k x 4k Matrix Transpose (K40c)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU (Core i7 4770) | 153.6 | 0.873 |  | 
Naive Transpose | 1.078 | 124.46 | 142.48 | 142.48
Coalesced Memory | 0.998 | 134.48 | 1.080 | 153.90
Bank Conflicts | 0.994 | 134.92 | 1.004 | 154.52
Loop Unrolling | 0.772 | 173.72 | 1.287 | 198.96

## Slide 56: Transpose
Let’s review your predictions!

## Slide 57: Reduction
Slide Credits: http://developer.download.nvidia.com/compute/cuda/1.1-Beta/x86_website/projects/reduction/doc/reduction.pdf

## Slide 58: Reduce
Algorithm to apply a reduction operation on a set of elements to get a result.
Example:
SUM(10, 13, 9, 14) = 10+13+9+14 = 46
MAX(10, 13, 9, 14) = 14
Reduction Slide Credits: http://developer.download.nvidia.com/compute/cuda/1.1-Beta/x86_website/projects/reduction/doc/reduction.pdf
Notes: Reduction: Any sequence of the same binary operation
Again, lets write your speedup on CPU
Hint: reduction is not as simple as transpose so don’t expect a similar speed up

## Slide 59: Serial Reduce
Loop through all elements
Number of steps: N - 1
+
+
10
13
9
+
14
46
Serial Code:
int result = IDENTITY;
for(int i = 0; i < N; i++) {
result = OP(result, array[i]);
}
Number of Steps : N = 4
Reduce[(10,13,9,14) +]

## Slide 60: Parallel reduce
Operations can be applied for Parallel reduce
Binary
  example: a*b, a+b, a&b, a|b
  not binary: !(a), (a)!
Associative
  example: a*b, a+b, a&b, a|b
  non associative: a/b, a - b
Example:
Reduce[(10,13,9,14) +]
+
10
13
9
+
14
46
+
Number of steps: log2 4 = 2
Notes: Most parallel reductions use a binary tree structure

## Slide 61: Parallel Reduce on GPU
Parallel reduce is applied to a part of the whole array in each block.
Multiple blocks help in:
  Maximizing Occupancy by keeping SMs busy.
  Processing very large arrays.
Parallel reduce is not arithmetic intensive, it takes only 1 Flop per thread(1 add) so it is completely memory bandwidth bounded.

## Slide 62: Parallel Reduce on GPU
Need a way to communicate partial results between blocks
Global sync is not practical due to the overhead of sync across so many cores
Solution: Call the reduce kernel recursively to reduce the results from previous reduce.
Level 0:
8 Blocks
Level 1:
1 Block

## Slide 63: Serial reduce vs Parallel reduce
Serial Reduce:
  Each iteration is dependant on the previous iteration.
  Runtime complexity is O(n)
Parallel Reduce:
  Has smaller number steps log2n.
  Faster than a serial implementation.
  Runtime complexity : O(log n)

## Slide 64: Reduction Code Walkthrough - Host
Single kernel call
Secondary reduction on CPU
Output data array size = ?

## Slide 65: Reduction Code Walkthrough - Device
Kernels Divided into 4 Parts:
Declare dynamic shared memory and compute index
Load input into shared memory
Reduce in shared memory
Copy result of each block into global memory
We only modify Parts 2 and 3 for optimization

## Slide 66: Stage 0: Interleaved Addressing

## Slide 67: Stage 0: Interleaved Addressing
__global__ void reduce_stage0(const float* d_idata, float* d_odata, int n) {
// Dynamic allocation of shared memory - See kernel call in host code
extern __shared__ float smem[];
int idx = blockIdx.x * blockDim.x + threadIdx.x; // Calculate 1D Index
if(idx < n)
smem[threadIdx.x] = d_idata[idx]; // Copy input data to shared memory
__syncthreads();
// Reduce within block - Start from c = 1, upto block size, each time doubling the offset
for(int c = 1; c < blockDim.x; c *= 2) {
if (threadIdx.x % (2 * c) == 0) // Add only on left index of each level
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
// Copy result of reduction to global memory
if(threadIdx.x == 0)
d_odata[blockIdx.x] = smem[0];
}
Part 1
Part 2
Part 3
Part 4
Notes: Walkthrough:
Compute index
Copy data to shared memory
Reduce interleaved in shared memory
Copy result to global

## Slide 68: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11

## Slide 69: Stage 0: Interleaved Addressing
Problem?

## Slide 70: Stage 0: Interleaved Addressing
Problem?
  Interleaved addressing
  Divergent warps
Solution?

## Slide 71: Stage 0: Interleaved Addressing
Problem?
  Interleaved addressing
  Too many divergent branches
Solution?
  Using modulo operator
  Non-divergent branches

## Slide 72: Warp Divergence

## Slide 73: Warp
A thread block is broken down to 32-thread warps
Warps are executed physically in a SM(X)
Total number of warps in a block: ceil(T/Wsize)
Up to 1024
Threads
32 threads each
Up to 64 Warps/SM (Kepler)

## Slide 74: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < 4) { x++; }else{ x--; }
Notes: Lets say warp size is 8
The warp is executing 3 commands instead of 2 (If statement is also a command)

## Slide 75: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < 4) { x++; }else{ x--; }

## Slide 76: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < 4) { x++; }else{ x--; }

## Slide 77: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < WARP_SIZE ) { x++; }else{ x--; }

## Slide 78: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < WARP_SIZE ) { x++; }else{ x--; }
Notes: Warp executes only 2 commands

## Slide 79: Warps - Take aways
Make threads per blocks to be a multiple of a warp (32)
  Incomplete warps waste unused cores
  256 threads per blocks is a good starting point
Try to have all threads in warp execute in lock step
  Divergent warps will use time to compute all paths as if they were in serial order

## Slide 80: ...back to reductions

## Slide 81: Stage 1: Remove Divergent Branching
Need to change the for-loop structure
Need the same values, just not the modulo etc
Restructure
// Reduce within block - Start from c = 1, upto block size, each time doubling the offset
for(int c = 1; c < blockDim.x; c *= 2) {
if (threadIdx.x % (2 * c) == 0) // Add only on left index of each level
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
Notes: Walkthrough:
Compute index
Copy data to shared memory
Reduce interleaved in shared memory
Copy result to global

## Slide 82: Stage 1: Remove Divergent Branching
__global__ void reduce_stage1(const float* d_idata, float* d_odata, int n) {
// Same as reduce stage 0
// Reduce within block
// Start from c = 1, upto block size, each time doubling the offset
// The difference here is that we eliminate modulo operator and the if condition
for(int c = 1; c > blockDim.x; c *= 2) {
int index = 2 * c * threadIdx.x;
// No divergence
if (index < blockDim.x)
smem[index] += smem[index + c];
__syncthreads();
}
// Copy result of reduction to global memory - Same as reduce stage 0
}
Part 3
Notes: Walkthrough:
Compute index
Copy data to shared memory
Reduce interleaved in shared memory
Copy result to global

## Slide 83: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41

## Slide 84: Stage 1: Remove Divergent Branching
Problem?
  Interleaved addressing
  Divergent warps
Solution?
  Using modulo operator
  Non-divergent branches

## Slide 85: Stage 0 & 1: Interleaved Addressing

## Slide 86: Stage 2: Sequential Addressing & Non-divergent Warps
Notes: Add 2 consecutive elements
After required steps, the element 0 will have the result

## Slide 87: Stage 2: Sequential Addressing & Non-divergent Warps
Still only need to change Part 2
Change the for loop such that offset is half of remaining size
What is start?
When is step?
What is end?
Notes: Add 2 consecutive elements
After required steps, the element 0 will have the result

## Slide 88: Stage 2: Sequential Addressing & Non-divergent Warps
What is start?
  c = blockDim.x / 2
When is step?
What is end?
Notes: Add 2 consecutive elements
After required steps, the element 0 will have the result

## Slide 89: Stage 2: Sequential Addressing & Non-divergent Warps
What is start?
  c = blockDim.x / 2
When is step?
  c = c / 2
  Is there a faster op for this?
What is end?
Notes: Add 2 consecutive elements
After required steps, the element 0 will have the result

## Slide 90: Stage 2: Sequential Addressing & Non-divergent Warps
What is start?
  c = blockDim.x / 2
When is step?
  c = c / 2
  Is there a faster op for this?
  Yes, c >>= 1
What is end?
Notes: Add 2 consecutive elements
After required steps, the element 0 will have the result

## Slide 91: Stage 2: Sequential Addressing & Non-divergent Warps
What is start?
  c = blockDim.x / 2
When is step?
  c = c / 2
  Is there a faster op for this?
  Yes, c >>= 1
What is end?
  c >= 1  c > 0
Notes: Add 2 consecutive elements
After required steps, the element 0 will have the result

## Slide 92: Stage 2: Sequential Addressing & Non-divergent Warps
__global__ void reduce_stage2(const float* d_idata, float* d_odata, int n) {
// Same as reduce stage 0/1
// Reduce within block
for(int c = blockDim.x / 2; c > 0; c >>= 1) {
// No need for index or modulo. It is replaced by c – similar to stage 0
if (threadIdx.x < c)
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
// Copy result of reduction to global memory - Same as reduce stage 0/1
}
Part 3
Notes: Walkthrough:
Compute index
Copy data to shared memory
Reduce interleaved in shared memory
Copy result to global

## Slide 93: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87

## Slide 94: Stage 2: Sequential Addressing & Non-divergent Warps
Problem?
  Last warp divergence?
  Memory Coalescing?
  Bank conflicts?
  How is thread usage?
Solution:
  Resolve bank conflicts.
for(int c = blockDim.x / 2; c > 0; c >>= 1) {
if (threadIdx.x < c)
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
Part 3

## Slide 95: Stage 3: Reducing Warp Wastage
In Stage 2
  1st iteration – Half threads per block are unused
  2nd iteration – 3/4 threads per block are unused
  3rd iteration – 7/8 threads per block are unused
  …..
We are not doing much work!
How to reduce wasted warps?
So what’s the solution?

## Slide 96: Stage 3: Reducing Warp Wastage
First – Launch only half the threads per block
  Get’s rid of maximum wastage
But, how to load data into shared memory?

## Slide 97: Stage 3: Reducing Warp Wastage
Add on Load!
  Each thread reads multiple values into shared memory
  So why not add on load too
  Doesn’t increase our global memory usage
  Also reduces the amount of shared memory we need
    Or keep shared memory same and do more work per block
First time we modify Part 2 of our kernel for optimization

## Slide 98: Stage 3: Add on load
14 | 15 | 64 | 12 | 87 | 67 | 54 | 75 | 40 | 19 | 5 | 23 | 48 | 56 | 25 | 52
54 | 34 | 69 | 35 | 135 | 123 | 79 | 127 | 59 | 19 | 28 | 23 | 104 | 56 | 77 | 52
656 | 319 | 148 | 162 | 135 | 123 | 79 | 127 | 59 | 19 | 28 | 23 | 104 | 56 | 77 | 52
Step 1:
Add 2 numbers when loading from global memory
Other Steps as before
0
1
2
3
4
5
6
7
Shared Memory
Notes: Instead of adding adjacent elements, add elements in adjacent blocks

## Slide 99: Stage 3: Add on load - Single
How would this look into code
We modify Part 2 of our kernel – Loading into shared memory
if(idx < n)
smem[threadIdx.x] = d_idata[idx];
__syncthreads();
Part 2
if(idx < n) {
smem[threadIdx.x] = d_idata[idx];
//Copy and add block data into shared memory
if(idx + blockDim.x < n)
smem[threadIdx.x] += d_idata[idx + blockDim.x];
}
Part 2

## Slide 100: Stage 3: Add on Load Multiple adds per thread
Replace single add with a loop.
Use a counter TILE to define the number to adds per thread
  defining TILE as global constant will allow loop unrolling
  preferable set TILE as power of 2
Notes: Substitute 2 adds per load by TILE adds per load.
Similar to loops in transpose

## Slide 101: Stage 3: Add on load - Multiple
Expand this to stage3_TILE adds on load
if(idx < n)
smem[threadIdx.x] = d_idata[idx];
__syncthreads();
Part 2
if(idx < n) {
smem[threadIdx.x] = 0; // Start with identity
for(int c = 0; c < stage3_TILE; c++) {
// Copy and add block data with block offset into shared memory
if(idx + c * blockDim.x < n)
smem[threadIdx.x] += d_idata[idx + c * blockDim.x];
}
}
Part 2

## Slide 102: Stage 3: Add on load - Multiple
__global__ void reduce_stage3(const float* d_idata, float* d_odata, int n) {
// Same as reduce stage 2
if(idx < n) {
smem[threadIdx.x] = 0; // Start with identity
for(int c = 0; c < stage3_TILE; c++) {
// Copy and add block data with block offset into shared memory
if(idx + c * blockDim.x < n)
smem[threadIdx.x] += d_idata[idx + c * blockDim.x];
}
}
// Copy result of reduction to global memory - Same as reduce stage 2
}
Part 2

## Slide 103: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87
Stage 3 (2 elements / thread) | 2.84 | 47.22 | 1.65 | 3.10

## Slide 104: Stage 3: Add on load - Multiple
Let’s change the tile factor and see how it affects performance
  TILE = 1?
  TILE = 2?
  TILE = 4?
  TILE = 8?
Notes: Half the warps are not doing anything because of the adding increment condition S >> =1

## Slide 105: Stage 3: Add on load - Multiple
Problem:
  Last warp is still divergent
Solution?
Notes: Half the warps are not doing anything because of the adding increment condition S >> =1

## Slide 106: Stage 3: Add on load - Multiple
Problem:
  Last warp is still divergent
Solution?
  Unroll the last warp
Notes: Half the warps are not doing anything because of the adding increment condition S >> =1

## Slide 107: Stage 4: Last Warp Unroll
Stage 2 Part 3 looks like:
Split it into 2 parts
Part 3A does same
  But stop at c <= 32
When c <= 32
  …
for(int c = blockDim.x / 2; c > 0; c >>= 1) {
if (threadIdx.x < c)
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
Part 3
for(int c = blockDim.x / 2; c > 32; c >>= 1) {
if (threadIdx.x < c)
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
if (threadIdx.x < 32)
// Do Something
Part 3A
Part 3B
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 108: Stage 4: Last Warp Unroll
When c <= 32
  This is where warp divergence comes in
  To remove warp divergence we’ll introduce a new warpReduce function
for(int c = blockDim.x / 2; c > 0; c >>= 1) {
if (threadIdx.x < c)
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
Part 3
for(int c = blockDim.x / 2; c > 32; c >>= 1) {
if (threadIdx.x < c)
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
}
if (threadIdx.x < 32)
warpReduce(smem, threadIdx.x);
Part 3A
Part 3B
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 109: Stage 4: Last Warp Unroll
Write a device function “warpReduce” to be called by all threads with threadIdx.x < 32
Observe that volatile is used to declare smem
  The compiler doesn't reorder stores to it and induce incorrect behavior.
  Basically – Tell compiler we know what we are doing
__device__ void warpReduce(volatile float* smem, int tid) {
//Write code for warp reduce here
smem[tid] += smem[tid + 32];
smem[tid] += smem[tid + 16];
smem[tid] += smem[tid + 8 ];
smem[tid] += smem[tid + 4 ];
smem[tid] += smem[tid + 2 ];
smem[tid] += smem[tid + 1 ];
}
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 110: Stage 4: Last Warp Unroll
So what’s the catch?
What’s different about this?
How did we get rid of the if conditions?
__device__ void warpReduce(volatile float* smem, int tid) {
//Write code for warp reduce here
smem[tid] += smem[tid + 32];
smem[tid] += smem[tid + 16];
smem[tid] += smem[tid + 8 ];
smem[tid] += smem[tid + 4 ];
smem[tid] += smem[tid + 2 ];
smem[tid] += smem[tid + 1 ];
}
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 111: Stage 4: Last Warp Unroll
So what’s the catch?
Essentially, when we write to the Nth part of the warp/block shared memory, we don’t really care about that data anymore
__device__ void warpReduce(volatile float* smem, int tid) {
//Write code for warp reduce here
smem[tid] += smem[tid + 32];
smem[tid] += smem[tid + 16];
smem[tid] += smem[tid + 8 ];
smem[tid] += smem[tid + 4 ];
smem[tid] += smem[tid + 2 ];
smem[tid] += smem[tid + 1 ];
}
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 112: Stage 4: Last Warp Unroll
Saves
  if (threadIdx.x < c)
  __syncthreads();
  Also saves useless work in all other warps – they exit early
Cost?
  Nothing – We are executing threads that were sitting idle before
__device__ void warpReduce(volatile float* smem, int tid) {
//Write code for warp reduce here
smem[tid] += smem[tid + 32];
smem[tid] += smem[tid + 16];
smem[tid] += smem[tid + 8 ];
smem[tid] += smem[tid + 4 ];
smem[tid] += smem[tid + 2 ];
smem[tid] += smem[tid + 1 ];
}
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 113: Stage 4: Last Warp Unroll
__device__ void warpReduce(volatile float* smem, int tid)
{
//Write code for warp reduce here
smem[tid] += smem[tid + 32];
smem[tid] += smem[tid + 16];
smem[tid] += smem[tid + 8 ];
smem[tid] += smem[tid + 4 ];
smem[tid] += smem[tid + 2 ];
smem[tid] += smem[tid + 1 ];
}
When smem[tid] += smem[tid + 16];
The first 16 have good values,
But the second half, we don’t really care about
We don’t need these anymore
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 114: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87
Stage 3 (2 elements / thread) | 2.84 | 47.22 | 1.65 | 3.10
Stage 4 (32 elements / thread) | 0.91 | 147.89 | 3.13 | 9.70

## Slide 115: Stage 4: Last Warp Unroll
One last improvement
Does the Stage 4 improvement inspire you?

## Slide 116: Stage 5: Complete Unroll
Taking inspiration from Stage 4
  Unroll the for loop entirely. (Part 3A)
  #pragma unroll requires sizes to be known at compile time
  Block size in GPU limited to 512 or 1024 threads.
    So there are only a limited number of if conditions we have to write
  Also make block sizes power of 2 (preferably multiples of 32).

## Slide 117: Stage 5: Complete Unroll
But block sizes is not known at compile time.
Solution :
  Use Templates
  CUDA supports C++ template parameters on device and host functions
  Specify block size as a function template parameter:
template <unsigned int blockSize>
__global__ void reduce4(int *g_idata, int *g_odata)
reduce_stage5<threads><<<dims.dimBlocks,
dims.dimThreads,
sizeof(float) * dims.dimThreads
>>>(d_idata, d_odata, n_elements);

## Slide 118: Stage 5: Complete Unroll
Loop Unroll:
if(blockSize >= 1024) {
if(threadIdx.x < 512) { smem[tid] += smem[tid + 512]; __syncthreads(); }
}
if(blockSize >= 512) {
if(threadIdx.x < 256) { smem[tid] += smem[tid + 256]; __syncthreads(); }
}
if(blockSize >= 256) {
if(threadIdx.x < 128) { smem[tid] += smem[tid + 128]; __syncthreads(); }
}
if(blockSize >= 128) {
if(threadIdx.x < 64) { smem[tid] += smem[tid + 64]; __syncthreads(); }
}
Part 3A

## Slide 119: Stage 5: Complete Unroll
The blockSize is known at compile time,
  All the code in red is evaluated at compile time.
No problem with other if conditions either
  All guarantee no warp divergence
if(blockSize >= 1024) {
if(threadIdx.x < 512) { smem[tid] += smem[tid + 512]; __syncthreads(); }
}
if(blockSize >= 512) {
if(threadIdx.x < 256) { smem[tid] += smem[tid + 256]; __syncthreads(); }
}
if(blockSize >= 256) {
if(threadIdx.x < 128) { smem[tid] += smem[tid + 128]; __syncthreads(); }
}
if(blockSize >= 128) {
if(threadIdx.x < 64) { smem[tid] += smem[tid + 64]; __syncthreads(); }
}
Part 3A

## Slide 120: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU (Intel Core i7 4770K) | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87
Stage 3 (2 elements / thread) | 2.84 | 47.22 | 1.65 | 3.10
Stage 4 (32 elements / thread) | 0.91 | 147.89 | 3.13 | 9.70
Stage 5 (32 elements / thread) | 0.87 | 154.18 | 1.04 | 10.11

## Slide 121: Performance Comparison

## Slide 122: But wait, there’s more
How do we improve performance further?
What assumption did we make about out starter code?

## Slide 123: But wait, there’s more
How do we improve performance further?
What assumption did we make about out starter code?
  NO RECURSIVE REDUCTION
  Call recursion on result of block reduction – instead of CPU

## Slide 124: Recursive Reduction
The way our code is structured, we can easily move it into separate function
Reduction kernel does not care about size
Our output data does not need to be preserved (except useful index)
So why not pass the output as the input
  And overwrite the output

## Slide 125: Recursive Reduction
The way our code is structured, we can easily move it into separate function
Reduction kernel does not care about size
Our output data does not need to be preserved (except useful index)
So why not pass the output as the input
  And overwrite the output

## Slide 126: But wait, there’s even more
Who can tell the difference between
  const float* x;
  float* const x;
  const float* const x;
Notes: Read it backwards (as driven by Clockwise/Spiral Rule)...
int* - pointer to int
int const * - pointer to const int
int * const - const pointer to int
int const * const - const pointer to const int
Now the first const can be on either side of the type so:
const int * == int const *
const int * const == int const * const

## Slide 127: But wait, there’s even more
The __restrict__ flag
  This flag is used to assure the compiler that the pointer marked by it do not overlap
  Basically, a and b are exclusive memory
  And that you will not do indexing that will overflow into the other
Compiler can make optimizations based on this
  Removes checks

## Slide 128: Conclusion
Understand CUDA performance characteristics
  Memory coalescing
  Divergent branching
  Bank conflicts
  Latency hiding
Use peak performance metrics to guide optimization
  Know peak GFLOPs and Memory Bandwidth of GPU
Know how to identify type of bottleneck
  e.g. memory, core computation, or instruction overhead
Optimize your algorithm, then unroll loops
Use template gracefully

## Slide 129: Stage 2: Sequential Addressing & Non-divergent Warps
Problem:
Bank conflict
  Each thread accesses adjacent memory locations resulting in shared memory bank conflict.
  2-way bank conflicts
Solution:
  Resolve bank conflicts.
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 

## Slide 130: Stage 2: Sequential Addressing & Non-divergent Warps
Problem:
Bank conflict
  Each thread accesses adjacent memory locations resulting in shared memory bank conflict.
  2-way bank conflicts
Solution:
  Resolve bank conflicts.
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  | 

## Slide 131: Stage 2: Sequential Addressing & Non-divergent Warps
Problem:
Bank conflict
  Each thread accesses adjacent memory locations resulting in shared memory bank conflict.
  2-way bank conflicts
Solution:
  Resolve bank conflicts.
Warp
B0 | B1 | B2 | B3 | B4 | ... | B30 | B31
0 | 1 | 2 | 3 | 4 | … | 30 | 31
32 | 33 | 34 | 35 | 36 | … | 62 | 63
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  |  | … |  | 
 |  |  |  | ... |  |